## Slide 1: Evaluating LLM Understanding a System Schema
Operative steps
Assess whether the LLM can comprehend the hardware system structure and interconnections
Determine whether a Json, descriptive or tabular representation is more effective
Test whether the model can infer dependencies between components and recognize interconnection patterns
Purpose: Validate whether the model accurately understands the system and its relationships before optimizing its diagnostic capabilities

## Slide 2: Preliminary Activities
State of the Art & Literature Review Results
Finetune/In-Context Learning improve performance
Structured data improve performance
A larger context confuses the model more
Quantization allows use of large models with little reduction in precision

## Slide 3: In-Context Learning and Prompt Engineering
ICL
Allows you to teach information to the model without training
No change in model weights
PE
Allows you to limit the output to a smaller space of possible values
Allows you to teach the model how to behave
Notes: Dall’attività delle settimane precedenti si è visto che con l’in-context learning è possibile controllare/limitare l’output del modello ad uno spazio ridotto di possibili valori. è quindi possibile insegnargli come rispondere agendo sul prompt, senza andare a modificare i pesi del modello.
Ed inoltre finetunare un modello può essere molto costoso in termini di risorse e richiede molti dati.

## Slide 4: Sample System
Console 1
eth0
Console 2
eth0
Console 3
eth0
SWITCH1
1
2
3
4
5
6
7
8
9
10
11
12
24
23
22
21
20
19
18
17
16
15
14
13
SWITCH2
1
2
3
4
5
6
7
8
9
10
11
12
24
23
22
21
20
19
18
17
16
15
14
13
Workstation 1
eth0
eth1
Workstation 2
eth0
eth1
Workstation 3
eth0
eth1
NAS
eth0
eth1
SERVER
Eth0
SWITCH3
1
2
3
4
5
6
7
8
9
10
11
12
24
23
22
21
20
19
18
17
16
15
14
13
SBC1
Eth0
Eth1
Eth2
SBC2
Eth0
Eth1
Eth2
SBC3
Eth0
Eth1
Eth2

## Slide 5: Components
Console
  computer equipped with a monitor, keyboard, and mouse, allowing operators to interact with a system
Switch
  a networking device that connects multiple computers or devices, efficiently managing data traffic within a network
Workstation
  A high-performance computer
SBC (Single Board Computer)
  A compact computer with all essential components (CPU, memory, I/O) integrated onto a single board, used in embedded systems.
NAS (Network Attached Storage)
  A dedicated storage device connected to a network, allowing multiple users to store and access files remotely.
Server
  A powerful computer that provides services or resources to other computers, managing data, applications, or networks.

## Slide 6: The prompt
Structure
Task description
Component definitions
Naming rules
Components list
Network/architecture topology
Q&A examples
Notes: Naming rules for questions, equal for all representations except few differences, in Json and tabular bidirectional connections are made explicit

## Slide 7: Textual representation
Naming rules and components

## Slide 8: Json representation
Naming/connection rules & data format

## Slide 9: Tabular representation
Naming rules & components

## Slide 10: Questions format
Q&A
Q&A generalized

## Slide 11: Dataset and accuracy
Dataset
94 questions and answers
Accuracy in
Reporting questions (always 100%)
Answer correctly

## Slide 12: First tests
Dash: {device name}-{device number}-{interface}
Colon: {device name}-{device number}:{interface}
Device name format | Run 1 | Run 2 | Run 3 | Mean
Colon | 85.0% (17/20) | 70.0% (14/20) | 100.0% (20/20) | 85.0%
Dash | 90.0% (18/20) | 87.5% (17.5/20) | 100.0% (20/20) | 92.5%
Llama3.2-3B-Instruct (8-bit quantization)

## Slide 13: Model limitations
Difficulty
Distinguish different objects with similar names (e.g., Switch-1, Switch-2)
-> Storage capacity related to the model size
Inference/reasoning

## Slide 14: Llama3.2-3B-Instruct results
Textual representation
Json representation
Device name format | Run 1 | Run 2 | Run 3 | Run 4 | Run 5 | Mean
Colon | 80.0% (24/30) | 93.3% (28/30) | 83.3 (25/30) | 80.0% (24/30) | 76.7% (23/30) | 82.66%
Dash | 63.3% (19/30) | 83.3% (25/30) | 83.3% (25/30) | 73.3% (22/30) | 90.0% (27/30) | 78.64%
Device name format | Run 1 | Run 2 | Run 3 | Run 4 | Run 5 | Mean
Colon | 86.7% (26/30) | 83.3% (25/30) | 73.3% (22/30) | 73.3% (22/30) | 86.7% (26/30) | 80.66%
Dash | 80.0% (24/30) | 83.3% (25/30) | 73.3% (22/30) | 83.3% (25/30) | 90.0% (27/30) | 81.98%

## Slide 15: Llama3.2-3B-Instruct results
Tabular representation
Device name format | Run 1 | Run 2 | Run 3 | Run 4 | Run 5 | Mean
Colon | 63.3% (19/30) | 70.0% (21/30) | 66.7% (20/30) | 80.0% (24/30) | 93.3% (28/30) | 74.6%
Dash | 86.7% (26/30) | 80.0% (24/30) | 50.0% (15/30) | 53.3% (16/30) | 63.3% (19/30) | 66.66%

## Slide 16: Smaller System
Console 1
eth0
Console 2
eth0
Console 3
eth0
SWITCH
1
2
3
4
5
6
7
8
9
10
11
12
24
23
22
21
20
19
18
17
16
15
14
13
Workstation 1
eth0
eth1
Workstation 2
eth0
eth1
NAS
eth0
eth1
SERVER
Eth0

## Slide 17: Smaller System results
Run 1 | Run 2 | Run 3 | Run 4 | Run 5 | Mean
88.2% (30/34) | 94.1% (32/34) | 91.2% (31/34) | 97.1% (33/34) | 94.1% (32/34) | 92.94%

## Slide 18: Phi-4-mini-reasoning results
(8-bit quantization)
Difficulty/limitations
Few tests due to hardware limitations
Run 1 | Run 2 | Run 3 | Mean 30q
96.7% (29/30) | 90.0% (27/30) | 84.0% (21/25) | 93.35%

## Slide 19: Mistral-7B-Instruct-v0.3 results
(4-bit quantization)
Difficulty/limitations
Prompt understanding
Run 1 | Run 2 | Run 3 | Run 4 | Run 5 | Mean
76.0% (19/25) | 64.0% (19/25) | 72.0% (18/25) | 72.0% (18/25) | 92.0% (23/25) | 75.2%

## Slide 20: Demo System
Console 1
eth0
Console 2
eth0
SWITCH
1
2
3
4
5
6
7
8
9
10
11
12
24
23
22
21
20
19
18
17
16
15
14
13
Workstation
eth0
eth1
NAS
eth0
eth1
SERVER
Eth0